## Slide 1: Life is Short: How Python Can Help Developing Intermittent System
PunchShadow
PyCon TW 2020
Sept 5, 2020
Notes: Title: 報告主題
Speaker's Name: 報告者的名字
Report Type: 填入報告類型, 例如: Paper Survey 或 Progress Report
Month Day, Year: 報告日期, 例如: Aug 10, 2012

## Slide 2: Who Am I ?
PunchShadow (謝宙穎)
  PhD student of NTUEE
Research domain:
  System & mircoarithecture design
  Non-volatile memory
Contact me
  NTU BL607
  Email: f07921043@ntu.edu.tw

## Slide 3: Outline
Introduction to Intermittent Computing
  Background
  Challenges
How Python Can Help
  Gem5
  pvlib
Appendix – Related Works

## Slide 4: What Causes Computing Intermittent ?
Let’s talk about Internet-of-Thing (IoT) first !

## Slide 5: Wait A Minute …
Have you ever considered about where the power of devices from ?
  Wire ? Battery ?
It’s impossible that all the edge devices could be connected through wire

## Slide 6: What’s The Problem of Battery ?
Have you ever feel your Iphone lack of power more and more quickly ?
THAT’S BATTERY AGING

## Slide 7: Why Don’t We Just Replace It ?
It’s available on our mobile phones, notebooks or vehicles.
But image if we have to change billions of devices which are deployed at the rainforest or inside our bodies ?
  Maintaining costs too much

## Slide 8: Here Comes Energy Harvester
Energy harvesting is the capture and conversion of small amounts of readily available environment energy into usable electrical energy
  Light energy: From sunlight or artificial light
  Kinetic energy: From vibration, mechanical stress or strain
  Thermal energy: Waste energy from heater, friction, engines,..
  RF energy: From RF signals

## Slide 9: Building Blocks of an Energy Harvesting
Use small battery or super capacitor to temporarily store the power which can offer the processing
  Smaller the capacitor, the more insignificant the aging problem is.

## Slide 10: It Turns to Other Problems
The reducing of capacitor makes the power supply unstable due to the rapid changing environment -> Intermittent power supply
Our target is to make processes execute correctly and efficiently under this condition.
[1] Hibernus: Sustaining Computation During Intermittent Supply for Energy-Harvesting Systems
[1]
Notes: [Fig.1 ] Hibernus: Sustaining Computation During Intermittent Supply for Energy-Harvesting Systems

## Slide 11: The Challenges We Face
Liveness Problem
Correctness Problem
Consistency Problem
Efficiency Problem

## Slide 12: Liveness Problem
Could finish a conventional program under intermittent system ?
  Checkpoint-based: statically or dynamically store data to non-volatile storage
  Task-based: Split large program to several small idempotent piece of atomic tasks
  Non-volatile memory based: Totally execute process on non-volatile memory or processor
    E.g. Disk/ SSD/ FRAM/ ReRAM/ MRAM

## Slide 13: Correctness Problem
Write-After-Read (WAR) problem
  Read and write at the same memory location will have WAR dependency
  Once the modified data have already stored in non-volatile memory, but the CPU doesn’t know it.
  Solution: data versioning, idempotent section…
[3] Alpaca: Intermittent Execution without Checkpoints

## Slide 14: Consistency Problem
CPU/MCU’s state can be checkpointed, but the peripheral devices’ state can’t be recorded.
  Incorrect results
  Infinite wait
  Timeliness and signal consistency
[3] Support Peripherals in Intermittent Systems with Just-In-Time Checkpoints

## Slide 15: Efficiency Problem
How and when to make a checkpoint is the best ?
  Re-execution cost vs. checkpoint overhead
  Which data we have to record ?
How to hide the long latency of non-volatile memory write ?
[4] Adaptive Dynamic Checkpointing for Safe Efficient Intermittent Computing

## Slide 16: When It Comes to Development
Acquire energy
Environment
Hardware Architecture
Software Application
Energy management
Crash consistency
Performance enhancement
NVM properties
Profiling
User resilient programming
Energy-aware framework
Crash consistency
OS/lightweight kernel support
Domain-specific questions
Variable energy sources
Energy harvester design
cooperation
Runtime issue

## Slide 17: Prior Method
Low power development board
Energy harvester
Take a lots of time on experiments
Constraint to design on hardware architecture
Hard to get the analysis data
Re-compile the program
+
+

## Slide 18: So What We Suggest Is...
Re-compile the program
Or change micro-op in gem5
+
+
simulator
Energy trace model
Fast to implement and easy to get the analysis data within gem5
Is flexible on micro-architecture design

## Slide 19: PVlib
A Python package to simulate the performance of photovoltaic energy systems
Convert TMY(Typical meteorological year) file to power trace
  Can customized some parameters, e.g. airmass, altitude,…

## Slide 20: gem5 Architecture
A modular platform for computer-system architecture research.
  A discrete event simulator
Use C++ object to represent physical system components
Completely controlled by Python Script
  Script define system to model
  All C++ objects exposed to Python
Source: http://learning.gem5.org/

## Slide 21: gem5 Architecture
Object
Object
Object
Object
Object
Python Script Configuration
SCons
pybind11
Modification on
architecture
build
C++
return
API
call

## Slide 22: SCons
A next-generation build tool.
Written in Python to support a variety of user interfaces
Customized Define target
  SimObject(‘DRAMSim2.py’)
Be careful when using Python2.7

## Slide 23: Pybind11
pybind11 is a lightweight header-only library that allows interacting with Python interpreter and writing Python extension modules in modern C++
  No dependencies, doesn’t require specific build tools
  Support almost every STL and class in C++
Source: Integrate Python and C++ with pybind11 - Robert Smallshire

## Slide 24: Pybind11 Example

## Slide 25: Object in pybind11
Object inheritance
C++
Python

## Slide 26: Object in pybind11
Function
C++
Python

## Slide 27: Object in pybind11
Read/ writeable parameter
C++
Python

## Slide 28: Magic of pybind11 in gem5
The py::module’s code is auto-generated by Python and Scons !!!!
Scons
Python
Class
C++
Object
M5 parser
Pybind module
scan
pass
Function transfer

## Slide 29: Magic of pybind11 in gem5

## Slide 30: More Details About pybind11

## Slide 31: Put It Together
Configure the architecture

## Slide 32: Put It Together
Add Energy Management Unit to the system

## Slide 33: Simple Energy Management
Calculate all the energy consumption of each component and compare it to the energy trace
Use state machine to represent the state changing corresponding to the energy
  If V < V_h: change to S_hibernating state

## Slide 34: Demo

## Slide 35: Reference
NVPSim:
  https://github.com/polarpolar/gem5-nvpsim
Gem5:
  http://learning.gem5.org/
  http://doxygen.gem5.org/release/current/index.html
Pybind11:
  https://github.com/pybind/pybind11
  https://www.youtube.com/watch?v=YReJ3pSnNDo&ab_channel=NDCConferences
  https://www.youtube.com/watch?v=jQedHfF1Jfw&ab_channel=EuroPythonConference
Scons:
  https://scons.org/
Pvlib:
  https://pvlib-python.readthedocs.io/en/stable/index.html

## Slide 36: Last But Not Least

## Slide 37: Q & A

## Slide 38: Appendix - Related Works
Hardware-based
  Ensuring idempotent: Clank
Software-based
  Just-in-time checkpoint: Hibernus
  Dynamic checkpoint: Chinchilla
  Peripheral devices: KARMA
Codesign
  Hide NVM latency: CoSpec

## Slide 39: Clank
Use hardware buffer to ensure the idempotent execution ( avoid WAR problem)
  Write-back buffer
  Watchdog timer
Drawback: buffer size, NVM latency
[5] Clank: Architectural Support for Intermittent Computation

## Slide 40: Hibernus
Use voltage detector to find out whether the voltage is under a certain threshold to make a checkpoint
Drawback: Frequent checkpoint
[1] Hibernus: Sustaining Computation During Intermittent Supply for Energy-Harvesting Systems

## Slide 41: Chinchilla
Dynamically shrink the interval of checkpoints to reduce the overhead
  Undo-logging to avoid WAR problem
  Compiler support for divide program to terminal checkpoint blocks
[4] Adaptive Dynamic Checkpointing for Safe Efficient Intermittent Computing

## Slide 42: KARMA
Record peripheral devices’ state and APIs to make a checkpoint and restore.
  Solve the inconsistency of CPU and I/O device state
[7] Intermittent Asynchronous Peripheral Operations

## Slide 43: CoSpec
Use pipeline to hide the long NVM write latency and speculatively commit to NVM
  Two phase commit to NVM
  Compiler support
[7] CoSpec: Compiler Directed Speculative Intermittent Computation